6.004 On-line: Questions for Lab 1 / When you're done remember to save your work by clicking on the "Save" button at the bottom of the page. You can check if your answers are correct by clicking on the "Check" button. / When entering numeric values in the answer fields, you can use integers (1000), floating-point numbers (1000.0), scientific notation (1e3), or JSim numeric scale factors (1K). / Problem 1. / Report the mosfet Ids you measured from the device curves for Vgs = 5V and Vds = 1.2V. / : / Compute the effective channel sheet resistance using (Vds)/(Ids) as an estimate for the channel resistance of the test mosfet. Don't forget to correct for the W/L of the test device! / : / Report the mosfet Ids you measured from the device curves for Vgs = 0V and Vds = 2.5V. / : / Calculate the time it would take to discharge a 0.05pF capacitor from 5V to 2.5V / : / Determine a scaled width (SW) for the two pullup mosfets so that the Vin and Vout curves for the NAND gate intersect at VDD/2 (1.65V). / : / What is the largest noise immunity we could specify and still have the NAND gate qualify as a legal device? Please fill in your answer with a precision of .01 volts. / Hint: to measure the low noise margin, use the VTC to determine what Vin has to be in order for Vout to be 3V, then subtract Vol (0.3V) from that number. To measure the high noise margin, use the VTC to determine what Vin has to be in order for Vout to be 0.3V, then subtract that number from Voh (3.0V). / : / Following standard practice, choose the logic thresholds as follows: / Vol = 10% of power supply voltage = 0.3V Vil = 20% of power supply voltage = 0.6V Vih = 80% of power supply voltage = 2.6V Voh = 90% of power supply voltage = 3.0V / Measure the contamination and propagation times for your NAND gate using both the falling and rising output transitions. / C for falling output (in seconds): / P for falling output (in seconds): / C for rising output (in seconds): / P for rising output (in seconds): / Use these measurements to compute estimates for an upper bound for tCD and a lower bound for tPD. / CD (in seconds): / PD (in seconds): / Recompute your bounds for tCD and tPD this time including the measurements you made at 100 degrees C. / CD (in seconds): / : / PD (in seconds): / : / source: on_line_questions.py, lab1questions.xdoc